## Slide 1: General Workflow of DTA Application: 4 Stages
A: Calibration
of FD, DTA queue model
B: DTA-based Congestion State Estimation
C: ODME for
OD-to-Count Consistence
D: Future Year
Scenario Analysis
Speed data
v(l,t)
Volume data
q(l,t)
Fundamental diagram
vf: free-flow speed
vc: critical speed
kc: critical density
m: Flow maximizing inertia factor
Congestion Bottleneck
Identification
P: Congestion duration
Volume from STA
D: Congested Demand
QHF: queued hour factor
Polynomial arrival rate parameters 
Estimated time dependent DTA volume and speed v'(l,t)
MAE, MAPE v'(l,t)-v(l,t)
Subarea OD from base year, Traffic Count C(l)
MAE, MAPE:
v‘’(l,t)-v(l,t)
x(l)-C(l)
Dynamic Traffic Assignment (DTA) and ODME
Updated OD demand matrix and link volume x(l)
Time dependent speed : v‘‘(l,t) consistent with OD
FY OD and FY link volume from STA
Updated FY OD demand matrix and link volume xfy(l)
Scenario Data
DTA queue evolution function calibration
MOE: vfy(l,t)-v(l,t)
xfy(l)-C(l)
Notes: We need to list both free-speed from the original model and reference speed from Inrix, and definition of LOS introduces potential inconsistency. Cleary define the critical speed, critical density for the congestion duration.
List from node id and to node id directly..
Show corridor/road id first and then show road order

## Slide 2: Fundamental diagram calibration
Example of calibrated speed-volume curve using S3 model
Calibration method: a recent 3-parameter model (S3 model) by Cheng et al., (2021)
v: speed
k: density
vf: free-flow speed
kc: critical density
m: shape parameter
Input: observed speed and density
Output: free-flow speed, critical density, shape parameter
Output: ultimate capacity
speed-density relationship
Cheng, Qixiu, Zhiyuan Liu, Yuqian Lin, and Xuesong Zhou. 2021. "An s-shaped three-parameter (S3) traffic stream model with consistent car following relationship." Transportation Research Part B: Methodological 153:246-71.

## Slide 3: Queue analysis
Cheng, Qixiu, Zhiyuan Liu, Jifu Guo, Xin Wu, Ram Pendyala, Baloka Belezamo, and Xuesong Zhou. 2022. "Estimating key traffic state parameters through parsimonious spatial queue models." Transportation Research Part C: Emerging Technologies 137:103596
Analysis method: a parsimonious spatial queue model by Cheng et al., (2022)
Assumption: the discharge rate is constant and arrival rate is cubic
Time dependent queue
Time dependent delay
Average delay

## Slide 4: QVDF calibration
Major steps towards queue-oriented link performance function QVDF
Zhou Simon, Xuesong, Qixiu Cheng, Xin Wu, Peiheng Li, Baloka Belezamo, Jiawei Lu, and Mohammad Abbasi. 2022. "A meso-to-macro cross-resolution performance approach for connecting polynomial arrival queue model to volume-delay function with inflow demand-to-capacity ratio." Multimodal Transportation 1 (2):100017

## Slide 5: QVDF calibration
Calibration method: a recent queue-based volume delay function by Zhou et al., (2022)
Assumption 2: Link magnitude of speed reduction and congestion duration
Assumption 1: Link congestion duration and D∕C ratio
P: congestion duration
fd: congestion duration constant
D: total inflow demand
C: ultimate capacity
n: oversaturation-to-duration elasticity factor
v_co: cut-off speed
v_t2: lowest speed in congestion duration
fp: MSR reduction constant
P: congestion duration
s: duration-to-speed reduction elasticity factor
Basic assumptions
Zhou Simon, Xuesong, Qixiu Cheng, Xin Wu, Peiheng Li, Baloka Belezamo, Jiawei Lu, and Mohammad Abbasi. 2022. "A meso-to-macro cross-resolution performance approach for connecting polynomial arrival queue model to volume-delay function with inflow demand-to-capacity ratio." Multimodal Transportation 1 (2):100017

## Slide 6: QVDF calibration
Calibration method: a recent queue-based volume delay function by Zhou et al., (2022)
Generate time-dependent delay
time-dependent queue
time-dependent delay
time-dependent speed
Generate time-dependent speed
Zhou Simon, Xuesong, Qixiu Cheng, Xin Wu, Peiheng Li, Baloka Belezamo, Jiawei Lu, and Mohammad Abbasi. 2022. "A meso-to-macro cross-resolution performance approach for connecting polynomial arrival queue model to volume-delay function with inflow demand-to-capacity ratio." Multimodal Transportation 1 (2):100017

## Slide 7: QVDF calibration
Calibration method: a recent queue-based volume delay function by Zhou et al., (2022)
Generate average speed
Generate average delay
Transition ratio
Generate largest delay
Zhou Simon, Xuesong, Qixiu Cheng, Xin Wu, Peiheng Li, Baloka Belezamo, Jiawei Lu, and Mohammad Abbasi. 2022. "A meso-to-macro cross-resolution performance approach for connecting polynomial arrival queue model to volume-delay function with inflow demand-to-capacity ratio." Multimodal Transportation 1 (2):100017